## Slide 1: Rehoboth Solar Project
Engineering W83

## Slide 2: Project Objective
What would it take for Rehoboth Christian School to construct, own, operate, and maintain a solar PV energy system?

## Slide 3: Site
Presented by: Claire Phillippi, Jack Amick, Jordan Veltema, Jordan Mast
Notes: Mast

## Slide 4: Outline
Work Accomplished
Location Options
  Decision Matrix
Climate
  Issues and Concerns
Installation Proposal
  Current Plan
  Future Options
Mounting System
Costs
Notes: Mast

## Slide 5: Work Accomplished
Survey
Decision Criteria
Decision Matrix
Meetings
Site Alternatives
Researched Cultural implications
Roof Loads Researched
Additional Weather Details
Final Construction Outline
Final Site Decisions
Notes: Mast

## Slide 6: Location Options
New High School
Existing Fitness Center
Existing Band Room
Fields
Carport
Bus Depot
Middle School
Dormitories
Notes: Mast

## Slide 7: Buildings
Notes: Mast

## Slide 8: Fields
Notes: Mast

## Slide 9: Carport
Notes: Mast

## Slide 10: Bus Depot
Notes: MAST

## Slide 11: Decision Criteria
Survey
Decision Matrix
  Aesthetics
  Placement
  Security
  Cost
  Ease of Construction
  Tie-In Distance
  Total Area
  Cleanliness
Notes: Mast

## Slide 12: Decision Matrix
Chart: 
| High School | Parking Lot | Fields (GROUND) | Dorms | Fitness Center | Middle School
 | 287 | 249 | 236 | 232 | 261 | 231
Notes: Mast

## Slide 13: Environmental Issues
Wind
Dust Accumulation
Precipitation
Temperature
Notes: Veltema

## Slide 14: Rehoboth Climate
Annual Average Wind Speed = 15.33 mph
Notes: Veltema

## Slide 15: Rehoboth Climate
Annual Average Precipitation = 12.55 inches
Notes: Veltema

## Slide 16: Rehoboth Climate
Notes: Veltema

## Slide 17: Rehoboth Climate
Notes: Veltema

## Slide 18: Wind on Roofs
Notes: Veltema

## Slide 19: Wind on Roofs
Notes: Veltema

## Slide 20: Installation Plan
New High School and Band Room
Fitness Center Roof
Future Options
Notes: Jack

## Slide 21: 1a. Band Room
Preexisting Structure
North
3600 ft2
0˚
Notes: Jack

## Slide 22: 1b. New High School
Future Structure
North
12192 ft2
0˚
Notes: Jack

## Slide 23: 2. Fitness Center
Preexisting Structure
6050 ft2
North
5˚ SW
Notes: Jack

## Slide 24: 3. Future Options
Middle School
  No structural plans or maximum roof loads available
Fitness Center (North Facing Roof)
  5 degree angle facing north east
New High School (Metal Roof)
  Not aesthetically pleasing
Notes: Jack

## Slide 25: Roof Materials
TPO Roofing
  Flat roof sections
  Cheaper to install onto
  Some obstructions
  20 year warranty, possible maintenance afterwards
Metal Roofing
  Slanted roof sections
  No obstructions
  No maintenance
Notes: Claire

## Slide 26: Ballast Mounting
Source: http://energyemp.com/
Notes: Claire

## Slide 27: Inclined Mounting
Notes: Claire

## Slide 28: Roof Loads
Existing roofs have room for 3 pounds per square foot
Band Room .9 psf
Fitness 1.42 psf
High School 1.28 psf
High School 1.51 psf
Fitness Center .9 psf
Notes: Claire

## Slide 29: Costs
  Racking system: $ 20,091
  Labor: $ 281,272 Total: $ 301,363
Upfront Costs
Notes: Claire

## Slide 30: Questions?

## Slide 31: Panel Selection
Presented by: Mr. Nate Hiemstra Mr. Mitch Hopkins
Mr. Mike Houtman
Mr. Tae-Hyung Lim
Mr. Josh Vanderkamp

## Slide 32: Outline
Status
  Overview
  Final Decisions
Work accomplished
  Panel Choice
  Panel Layout
  Energy Yield
  Cost Analysis
  Obstacles
Future Plan
  3 Possibilities

## Slide 33: Monocrystalline
The most efficient type of solar panels (about 15-20%)
More expensive
Ideal for roofs
Notes: Made out of silicon ingots
If the solar panel is partially covered with shade, dirt or snow, the entire circuit can break down.

## Slide 34: Polycrystalline
Less cost
Efficiency of approximately 13-16%
Performance decreases at higher temperatures

## Slide 35: Thin-Film Solar Panels
Categories by material
  Amorphous silicon (a-Si)
  Cadmium telluride (CdTe)
  Copper indium gallium selenide (CIS/CIGS)
  Organic photovoltaic cells (OPC)
Efficiencies between 7–13%
Mass-production is simple
Can be made flexible
Strong against high temperatures and shading

## Slide 36: Thin-Film Solar Panels
Spatial limitations (about 4 times more space needed)
Structural costs
Degrade faster over time

## Slide 37: Building-Integrated Photovoltaics (BIPV)
Expensive
Good looks but less efficient
Easy installation

## Slide 38: Suggestions
Limitations
  Space - Monocrystalline Silicon, BIPV
  Cost – Thin Film, Polycrystalline
Install Site
  Rooftop – Crystalline Silicon, BIPV
  Field – Thin Film
  Parking lot shade – Thin Film, Crystalline Silicon

## Slide 39: Panel Types
8 Criteria Weighted:
  Panel Efficiency (18%)
  Cost (23%)
  Weight (9%)
  Size (5%)
  Rated Power (15%)
  Company Reputation (8%)
  Aesthetics (10%)
  Warranty/Degradation (12%)
5 Panels Compared:
  SunPower E20 327W Mono
  Yingli 270W Mono
  Yingli 310W Poly
  SolarWorld 245W Poly
  SunPower E18 305W Mono
Notes: Leads to Decision Matrix

## Slide 40: Decision Matrix
Chart: 
SunPower E20-327 | 3.285
YL270C-30b | 2.7
Yingli YL310P-35b | 3.13
SW 245 poly (solarworld) | 2.67
SunPower E18 / 305 SOLAR PANEL | 3.45
SunPower E20 327W
Yingli YL270
270W
SolarWorld Poly 245W
SunPower E18 305 W
Notes: Sunpower E18 is Best

## Slide 41: Panel Choice
SunPower E20/327
  20.1% efficient
  327 Watts
  Degrades at 0.25% yearly
  25 year warranty

## Slide 42: Energy Yield
Goal to offset 50% of annual consumption due to power company constraints
  296,000 kWh annual yield
Notes: Looked at all areas

## Slide 43: Panel Layout Factors
Panel Spacing
  Roof obstacles
  6 ft from roof edges
  2 ft spacing between panels
Panel Orientation
  15 degrees
  Standard to mounting system
  Aesthetics

## Slide 44: Fitness Center
192 Panels
108,300 kWh
N
Notes: Jack

## Slide 45: New High School/Band Room
320 Panels
183,200 kWh
N
Notes: Jack

## Slide 46: Total System Overview
512 Panels
291,500 kWh
47% of total energy consumption
N
Notes: Jack

## Slide 47: System Costs
  Panel: $ 210,944
  Total: $ 210,944
Upfront Costs
  Replacement Units (% 0.05 Upfront) $ 2,845
  Labor: $ 60 Total: $ 2,905
Annual Costs
Notes: Claire

## Slide 48: Obstacles
Fitness Center Loads
  Obtain official civil engineering approval
New High School Design Loads
  Civil Engineering design work for additional loads

## Slide 49: Fitness Center North Roof
288 Panels
150,300 kWh
73.2%
Pros: Not visible from ground, large space available, close to flat
Cons: North facing, loss of ~8% energy production

## Slide 50: New High School (cont.)
192 Panels
114,300 kWh
67.1%
Pros: Faces directly South, 15 degree incline
Cons: Aesthetics, small area compared to alternatives

## Slide 51: Middle School
480 Panels
283,300 kWh
95.7%
Pros: large space available, South facing, ~50% additional energy production
Cons: Lack of building information (age, structure, loading capability, etc…)

## Slide 52: Questions?

## Slide 53: Inverters
Presented by: Brandon Koster, Andrew Vriesema, and Lukas Woltjer

## Slide 54: Outline
Introduction
Considerations for Selection
Equipment Selection
  Inverter Type
  Sunny Design Optimization
  Monitoring Options
  Tie in, Combiner Boxes, Panels, and Cutoff Switches
System Design and Location
Areas of Concern
Questions

## Slide 55: Introduction
Purpose of Inverters
  DC to AC
  Power Quality
Importance of Monitoring
  Ensure Maximum Production
  Alerts for Equipment Failure

## Slide 56: AC and DC
Image source: Wikipedia

## Slide 57: Power Quality
http://oikos.com/library/energy_outlet/pq.gif

## Slide 58: Monitoring
http://www.sunterrasolar.com/
Notes: Monitoring checks to make sure that all inverters are performing equally. If they are not, then it is likely that panels are shaded or some equipment has failed.

## Slide 59: Equipment Selection
Cost
Reputation
Ease of installation and maintenance
Compatibility with existing equipment

## Slide 60: Inverter Types
Micro inverters
String inverters
Central inverter

## Slide 61: Inverter Cost Comparison

## Slide 62: Cost Estimations
String Inverters (SB-8000TLUS) $0.27 / Watt
Central Inverter (SMA SC-125U) $0.26 / Watt
Central Inverter (Solectrica 75kW) $0.31 / Watt
Notes: SC-125U no longer available, used for system model

## Slide 63: Micro Inverters
http://leosunergy.com/images/solar-inverter-technology.jpg
Notes: One per panel
Enables accurate monitoring
Maximizes power production
High cost per watt

## Slide 64
http://gigaom2.files.wordpress.com/2008/09/enlighten-nichols-residence2.jpg

## Slide 65: Micro Inverter Advantages
Each panel is constantly optimized for highest production
Entire string does not suffer for shading on one panel
Production of each panel can be monitored
Troubleshooting the system is very easy

## Slide 66: Micro Inverter Disadvantage
Highest cost per watt

## Slide 67: Micro Inverters
http://leosunergy.com/images/solar-inverter-technology.jpg
Notes: One per panel
Enables accurate monitoring
Maximizes power production
High cost per watt

## Slide 68: Central Inverter
www.abcsolar.com
Notes: SMA central inverters start at 250 kW. Other central inverters come as small as 100 kW.

## Slide 69: Central Inverter Advantages
Lowest cost per watt
Fewer inverters to operate and maintain

## Slide 70: Central Inverter Disadvantages
Array would be very large and potentially difficult to monitor and troubleshoot
New DC lines would have to be run to the location of the inverter

## Slide 71: Central Inverter
www.abcsolar.com
Notes: SMA central inverters start at 250 kW. Other central inverters come as small as 100 kW.

## Slide 72: String Inverters
www.sma-america.com
Notes: Generally handles 2-5 strings, up to 600 volts
Similar cost per watt to central inverters. Substantially cheaper than micro inverters

## Slide 73: String Inverters
Notes: Generally handles 2-5 strings, up to 600 volts
Similar cost per watt to central inverters. Substantially cheaper than micro inverters

## Slide 74: Wall Mount Advantages
Most commonly produced inverter
A few strings come together to form an independent array
Smaller capacities allow easy integration to existing building electrical systems
Easier monitoring of production than ground mount commercial inverters

## Slide 75: Wall Mount Disadvantages
Higher cost per watt than ground mount commercial inverters
More inverters to install, operate, and maintain

## Slide 76: Transformer Types
Transformer
  Proven reliability
  Less efficient
  Larger and heavier
Transformerless
  Use a multi-step computerized process to invert DC power
  Lighter design
  Higher efficiency
  Must have ungrounded wiring, held to higher safety standards
  Additional overcurrent protection required
Recommend Transformerless

## Slide 77: Inverter Selection

## Slide 78: Inverter Selection
SMA Sunny Boy transformer-less (SBxxxxTL-US) series inverters
  High efficiency
  Light weight
  Competitive cost per watt
  Able to tie into single and three phase electrical systems
  Available in different sizes

## Slide 79: Sunny Design
Used to select inverters for a specified type and number of panels
Chose inverters and panel wiring options for 100% power ratio

## Slide 80: Sunny Design

## Slide 81: Monitoring Options
Notes: Monitoring systems can be inverter integrated or be an extra component. ECHS used DECK to handle the data, and recommends them.
ALSOenergy quoted “less than 1% of total system cost”

## Slide 82: Monitoring Recommendation
Use installer-recommended provider
No accurate quotes to date
Cost: less than 1% of total system cost (ALSOenergy)
Eastern Christian High School has used DECK monitoring

## Slide 83: Grid Tie-in Equipment
Load centers (breaker panels)
AC safety disconnect switches
Wiring and conduit

## Slide 84: Tie-In Diagram
Source: www.energy.ca.gov
Notes: First three elements are generally built into inverter.
Two AC disconnects are for convenience when working on the inverter.

## Slide 85: Tie-In Restrictions
Agreement for Parallel Connection
  System of up to 75 kW in parallel with the grid
  Commercial Agreement
Can connect to grid once the following conditions are met:
  Agreement signed
  Installation complies with Appendix A
  Installation inspected by State CID Electrical Inspector
  Approval Form signed by CID and GJU
  Appendix B signed
GJU has right to terminate agreement within 30 days written notice
Notes: CID = Construction Industries Division

## Slide 86: Appendix A
RRGS and associated equipment complies with:
  UL Standards
  Applicable IEEE Standards
  2005 National Electric Code
  State and Local Codes and Regulations
Prior to installation
  Agreement needs to be executed
  Applicable permits obtained
Prior to Connection
  Inspection by GJU and CID
  Anti-Islanding and Power Quality Inspected and Tested
  An accessible, manual, lockable load break disconnect between inverter output and connection to grid
  Permanent weatherproof diagram of the system at metering point

## Slide 87: Appendix A: Net Metering
Apply for Net Metering after Agreement has been executed
Excess energy results in a credit that will be applied to the account and carried from month to month
GJU can reconcile the account annually by buying-back the credits
Liability Protection
Appendix B

## Slide 88: Conversations with GJU
75 kW is negotiable
Might have to pay a flat fee
Must go before city council
GJU has never ruled on a proposal above 75 kW

## Slide 89: Placement Options
Parapet Wall
Side Wall
  Near Meter

## Slide 90: Costs
  SunnyBoy 5000 TL (3): $ 6,642
  SunnyBoy 8000 TL (2): $ 4,548
  SunnyBoy 10000 TL (13): $ 39,806
  Deck Monitoring System: $ 5,633
  Tie-in components: $ 4,226
  Total: $ 60,855
Upfront Costs
Notes: Claire

## Slide 91: Issues and Concerns
School electrical system
  Can tailor PV system for multiple grid configurations
Integrating monitoring system
  Waiting for DECK about integration with SMA inverters
75kW limit set by Gallup
  Negotiate 150 kW system, tied in at two locations

## Slide 92: Questions?

## Slide 93: Financial
Presented by: Allen Bosscher, Karl Bratt, Jonathan Haines
Notes: JON

## Slide 94: Outline
Work Accomplished
Issues and Concerns
Next Steps
Summary
Questions
Notes: JON

## Slide 95: Work Accomplished
Financing Options
Additional Grant & Tax Incentives
Electric Bill Analysis
PPA & Solar Lease Research
Cost Models and Analysis
L.L.C. Research
Notes: JON

## Slide 96: Financing Options
Direct Financing
Limited Liability Corporation
Power Purchase Agreement
Solar Lease

## Slide 97: Direct Financing
Process
PV System is Purchased
Donation vs. Loan
Advantages
Independent
Higher Potential
One-time Cost
Disadvantages
High Upfront Cost
Responsible for Damages
Non-profit Company
High Risk

## Slide 98: Privately Owned L.L.C.
Process
Donation vs. Loan
Roof is Rented Property
Billed for Electricity
  At least 50% utility cost rate
Annual donation of revenue back to school (lawyer)
Advantage
For-profit federal and state tax incentives

## Slide 99: Power Purchase Agreement
Process
Roof is Rented Property
PV System 3rd Party Owned
Billed for Electricity Usage
Advantages
For-profit federal and state tax incentives
Reduced Cost of Electricity
No Upfront Cost
Disadvantages
20-25 Year Contract

## Slide 100: Solar Lease
Process
PV System is Leased
Set Monthly Payment
Advantages
For-profit federal and state tax incentives
Set Monthly Payment
Low Upfront Cost
Disadvantages
20-25 Year Contract
Responsible for Damages

## Slide 101: Grant Possibilities
USDA High Energy Cost Grant
  Federal Grant
  Applicable to: Nonprofits and Schools
  Max Incentive = $3 million
  Eligible in areas where average home energy costs are 275% above national average
    NOT applicable to Rehoboth
      New Mexico Avg. Home Energy Cost = $0.0809/kWh
      National Avg. = $0.113/kWh

## Slide 102: Grant Possibilities
USDA Rural Energy for America Program (REAP)
  Federal Grant
  Applicable to: “Schools”
  $2,500 - $500,000
  Max Incentive = 25% of total project cost
  Eligible for colleges and universities
    NOT applicable to Rehoboth (K-12 School)
  Might be available with a L.L.C.

## Slide 103: State Incentives
New Mexico Corporate Tax Credit
  6% tax credit
  Max incentive = $60 million
  Applicable to commercial sector
Sustainable Building Tax Credit
  Based upon LEED certification
  $0.30 - $6.25/ft2
Non-profit = No tax
  Receive credit and sell to a for-profit entity

## Slide 104: Federal Incentives
Business Energy Investment Tax Credit
  30% Tax Credit on Capital Investment
  No Max Incentive
  Applicable to commercial sector
Applicable To:
  PPA
  Solar Lease
  L.L.C.

## Slide 105: Electricity Invoice Analysis
Chart: Monthly Energy Demand Charges Rehoboth 2012-2013
| June, 2012 | July | August | September | October | November | December | January, 2013 | February | March | April | May
Cost per kWh | 2965.2 | 2866.36 | 3607.66 | 3854.76 | 3657.08 | 4250.12 | 3311.14 | 4892.58 | 3360.56 | 3558.24 | 3360.56 | 3014.62
Environmental Surcharge | 200.11 | 192.18 | 249.66 | 259.54 | 235.73 | 251.5 | 221.89 | 285.15 | 219.9 | 219.85 | 215.92 | 190.15
Usage Surcharge | 1370.03 | 1370.03 | 1370.03 | 1370.03 | 1370.03 | 1370.03 | 1370.03 | 1370.03 | 1370.03 | 1370.03 | 1370.03 | 1370.03
Additional kW Surcharge | 667.4 | 568 | 1263.8 | 1263.8 | 866.2 | 667.4 | 866.2 | 866.2 | 766.8 | 568 | 667.4 | 369.2
Annual Total = $ 69,892
Notes: KARL

## Slide 106: Electricity Invoice Analysis
Chart: Monthly Energy Projection Rehoboth 2014
| June | July | August | September | October | November | December | January | February | March | April | May
Cost per kWh | 3322.2 | 3211.46 | 4042.01 | 4318.86 | 4097.38 | 4761.82 | 3709.79 | 5481.63 | 3765.16 | 3986.64 | 3765.16 | 3377.57
Environmental Surcharge | 197.4 | 190.82 | 240.17 | 256.62 | 243.46 | 282.94 | 220.43 | 325.71 | 223.72 | 236.88 | 223.72 | 200.69
Usage Surcharge | 1534.43 | 1534.43 | 1534.43 | 1534.43 | 1534.43 | 1534.43 | 1534.43 | 1534.43 | 1534.43 | 1534.43 | 1534.43 | 1534.43
Additional kW Surcharge | 747.3 | 636 | 1415.1 | 1415.1 | 969.9 | 747.3 | 969.9 | 969.9 | 858.6 | 636 | 747.3 | 413.4
Difference ≈ $10,000
Annual Total = $ 79,621
Notes: KARL

## Slide 107: Electricity Rate Analysis
Tier Bill Sections | General Service Medium | General Service Small
First 100 kW or Less ($) | 1,534.43 | -
Additional Demand ($/kW) | 15.90 | -
First 100 kWh ($) | - | 14.45
Energy Charge ($/kWh) | 0.0791 | 0.1285
General Service Medium Requirements:
For 3 Consecutive Months…
  40,000 kWh Monthly Usage
  100 kW
  Monthly Peak Usage
  ~OR~
Notes: KARL

## Slide 108: Electricity Rate Analysis
Chart: Gallup Joint Utilities General Small vs. Medium Rate Schedules
Small | 14.45 | 134.33 | 267.53 | 400.73 | 533.93 | 667.13 | 800.33 | 933.53 | 1066.73 | 1199.93 | 1333.13 | 1466.33 | 1599.53 | 1732.73 | 1865.93 | 1999.13 | 2132.33 | 2265.53 | 2398.73 | 2531.93 | 2665.13 | 2798.33 | 2931.53 | 3064.73 | 3197.93 | 3331.13 | 3464.33 | 3597.53 | 3730.73 | 3863.93 | 3997.13 | 4130.33 | 4263.53 | 4396.73 | 4529.93 | 4663.13 | 4796.33 | 4929.53 | 5062.73 | 5195.93
32,000 kWh
Notes: KARL

## Slide 109: Electricity Rate Analysis
Chart: Gallup Joint Utilities Cost of Electricity Growth Rate
| 2005 | 2006 | 2007 | 2008 | 2009 | 2010 | 2011 | 2013
Cost Per kWh | 0.0504 | 0.0541 | 0.0554 | 0.0579 | 0.058 | 0.0643 | 0.0706 | 0.0791
Additional Surcharge | 11.06 | 12.05 | 12.34 | 13.1 | 13.13 | 13.66 | 14.2 | 15.9
Average ≈ 5%

## Slide 110: PPA & Solar Lease Research
Contacts
Patricia Mattioli
  Consolidated Solar Technologies
Mark Durmmond
  Positive Energy Solar
Notes: JON

## Slide 111: Cost Modeling

## Slide 112: Cost Modeling

## Slide 113: Cost Modeling
  Site $ 301,363
  Panel $ 210,944
  Inverter $ 60,855
  Total: $ 573,162
TOTAL Upfront Costs
  Panel $ 2,905
  Total: $ 2,905
TOTAL Annual Costs
Notes: Claire

## Slide 114: Cost Modeling

## Slide 115: Cost Modeling
Chart: Rehoboth Solar Project 30 Year Forecast of Financing Alternatives
| 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24 | 25 | 26 | 27 | 28 | 29 | 30
Direct Financing | -568936.232 | -531769.2802 | -493406.3288 | -453814.9434 | -412961.7219 | -370812.2679 | -327331.1619 | -282481.9327 | -236227.0275 | -188527.7813 | -139344.3852 | -88635.854 | -36359.9929 | 17526.637 | 73068.7541 | 130312.3927 | 189304.9405 | 250095.1771 | 312733.3137 | 377271.0339 | 443761.5357 | 512259.5749 | 582821.5093 | 655505.3446 | 730370.7817 | 807479.2646 | 886894.031 | 968680.1629 | 1052904.6398 | 1139636.393 | 1228946.3613
L.L.C | -398255.3624 | -364805.1057 | -330278.4495 | -294646.2026 | -257878.3033 | -219943.7947 | -180810.7994 | -140446.4931 | -98817.0784 | -55887.7568 | -11622.7002 | 34014.9778 | 81063.2528 | 129561.2197 | 179549.1251 | 231068.3998 | 284161.6929 | 338872.9058 | 395247.2288 | 453331.1769 | 513172.6286 | 574820.8638 | 638326.6048 | 703742.0566 | 771120.9499 | 840518.5846 | 911991.8743 | 985599.393 | 1061401.4222 | 1139460.0001 | 1219838.9716
PPA | 0 | 20420.2352 | 41428.8417 | 63042.7722 | 85279.468 | 108156.8729 | 131693.4478 | 155908.1855 | 180820.6259 | 206450.8721 | 232819.6063 | 259948.1066 | 287858.2644 | 316572.6016 | 346114.2891 | 376507.1656 | 407775.7565 | 439945.2938 | 473041.7366 | 507091.7921 | 542122.9367 | 578163.4388 | 615242.3811 | 653389.6844 | 692636.1314 | 733013.392 | 774554.0485 | 817291.622 | 861260.5993 | 906496.4612 | 953035.7105
Solar Lease | 0 | 20720.8285 | 42088.2607 | 64122.474 | 86844.2758 | 110275.1225 | 134437.1402 | 159353.1455 | 185046.667 | 211541.9674 | 238864.0666 | 267038.7653 | 296092.6693 | 326053.2146 | 356948.6933 | 388808.2806 | 421662.0619 | 455541.0616 | 490477.272 | 526503.6839 | 563654.3177 | 601964.2552 | 641469.6731 | 682207.8769 | 724217.3362 | 767537.7214 | 812209.9403 | 858276.1777 | 905779.9346 | 954766.0695 | 1005280.8407
≈ 23 Years
10 Years
12 Years

## Slide 116: Effective Rates
Chart: 25 Year NPV Cost of Energy ($/kWh)
| No Solar | Donation Direct Purchase | Donation L.L.C. | Solar Lease | PPA
 | 0.14148 | 0.085964 | 0.062542 | 0.068922 | 0.07

## Slide 117: Issues & Concerns
Solar Lease Quote
75 kW Capacity Limit
Legal Concerns with School Owned L.L.C.
Cost Flow Assumptions
Donation Fundraising
Financial Institution Financing
Notes: JON

## Slide 118: Next Steps
Poster 1/28
Final Report 1/28
Solar Lease Quote 1/30
Engineering Department Seminar 2/12
Notes: KARL

## Slide 119: Summary
What would it take for Rehoboth Christian School to construct, own, operate, and maintain a solar PV energy system?
Rehoboth Strategic Objectives:
  Offset 50% of total electricity demand by 2020
  Focus on managing school, not managing energy infrastructure
Notes:     Prefer to minimize energy aspect
    Remove as much responsibility as possible
    Place responsibility on outside company

## Slide 120
We recommend that Rehoboth install a 167 kW Solar PV system in 2015, financed by a Solar Lease
N

## Slide 121: Questions?
Notes: KARL