## Slide 1: Biofuel Production & Implementation Feasibility Study
A Proposal for Calvin College
Presented By: Engineering 333 & Business 380

## Slide 2: Project Objective
What would it take to operate a biofuel vehicle using only on-campus resources?
Feedstock
Application
Transportation
Processing Plant
Waste
Biofuel Vehicle
Notes: Explain Process more thoroughly

## Slide 3: Project Segmentation
Technical Feasibility
Fuel Selection
Vehicle Selection
Facilities Selection
Future Planning
Students
Prospective Students
Faculty/Staff
Alumni/Community
Donors
Decision-Makers
Messaging & Communication
Notes: Talk to the audience

## Slide 4: Resources
Prof. Matthew Heun – Engineering Department
Prof. Thomas Betts – Business Department
Mr. Phil Beezhold – Physical Plant Director
Mr. David LaGrand – Local Biofuel Producer
Mr. Geoffrey Van Berkel – Physical Plant Grounds
Mr. Rick Balfor – Dining Services
Mr. Rich Huisman – Chemistry Department
Mr. Henry Kingsma– Physical Plant Recycling

## Slide 5: Fuel Production and Feedstock
Presented by: Claire Philippi

## Slide 6: Processing?
Fuel?
Feedstock
Vehicle Application

## Slide 7: Fuel Options
Image source: nationalgeographic.com
Methane
Image Source: baconsrebellion.com
Ethanol
Image Source: biodieselchemist.webs.com
Biodiesel
Image Source: zombiehunters.org/wiki
Vegetable Oil
Feedstock
Vehicle Application
Notes: These are the 4 original fuel options. Describe method of choosing the WVO.
Methane via compost
-Forms mushroom clouds
-requires conversion
Ethanol via grass clippings
Biodiesel via vegetable oil and alcohol reaction
Vegetable Oil
-you can run a diesel engine on waste vegetable oil
http://ngm.nationalgeographic.com/2012/12/methane/thiessen-photography#/01-methane-bubbling-from-arctic-lake-670.jpg
http://biodieselchemist.webs.com/
http://www.baconsrebellion.com/2013/09/suspicious-trading-in-gas-ethanol-credits.html
http://www.zombiehunters.org/wiki/index.php/Waste_Vegetable_Oil
l

## Slide 8: Fuel Quality
Image Source: journeytoforever.org/biodiesel_svo
Fuel Clarity
Image Source: titrations.info
Acidity
Vehicle Application
Notes: Here is a pic of various oil qualities. Ours is less than E which gave us cause for concern. This implies that we need very good filtration and possible chemical additives to neutralize the oil.
http://journeytoforever.org/biodiesel_svo.html#gnl
http://www.titrations.info/acid-base-titration-indicators-preparation
FFA was the main concern for the oil. Through research it was shown that FFA can be very detrimental to the process if the concentration is too high. In order to determine the concentration of the FFA a titration test was done by Rich Huisman from the Chemistry department. Researched provided us with a step by step test to determine the FFA concentration of our WVO. Simply put a chemical indicator called, phenolphthalein, was added to the oil and the amount of phenolphthalein that caused the oil to turn a pink color determined the concentration of the FFA. If the amount of phenolphthalein added was less than 3mL then the sample would be considered ok to use.
Free Fatty Acid
  Concern: The amount of Free Fatty Acid would be too high in the WVO that it would be corrosive to the entire system

## Slide 9: Filtration Methods
Image Source: filterbag.com
Image Source: wvodesigns.com
Image Source: threedeadflies.com
Vehicle Application
Notes: Requirement: 5 micron filtration
Stages: Typical filtration includes filtering in stages. 400-200-100-50-10-5. This increases the life of the filters because in decreases the likelihood of clogging the smaller filters
Time: 200-300 Gal/Filter for good oil, 20-30 Gal/filter for bad oil
Change Frequency: Once a month for good, 10 times a month
Filters
  Requirement
  Stages
  Time
  Filter Change Frequency
http://www.filterbag.com/Waste-Vegetable-Oil-Filtration-16.html
http://www.wvodesigns.com/shop/centrifuges/rpc-basic.html
http://www.threedeadflies.com/settlingtank.asp

## Slide 10: Costs
The Upfront Component Costs:
  Centrifuge and heating source: $1494
  Settling tanks: $ 428
  Filter and screens: $ 50
  Total: $1972
Vehicle Application
Monthly Operating Costs:
  Filters & Screens $ 4
  Heat $ 10
Notes: Equipment costs
Everyone else will have equipment costs

## Slide 11
Facilities & Infrastructure
Presented By: Karl Bratt

## Slide 12: How to Process?
Where to Process?
12
Vehicle Application

## Slide 13: WVO Processing Location
Physical Plant Warehouse
Vehicle Application
Notes: Options:
Physical Plant Warehouse
Boiler Room Under Commons
Moveable Trailer
Reasons:
Ownership
Ease of Accessibility
Climate Control
Shelving
Under Utilized
120 Sq. Ft Available

## Slide 14: Shelving
Industrial Racking System
Vehicle Application
Notes: Options:
Custom-Built System
Industrial Racking System
Reasons:
Present Currently
Customizable
OSHA Requirements
Weight Requirements

## Slide 15: Heating
Existing Heater & Heating Tape
Vehicle Application
Notes: Options:
Existing Heater
Heating Blanket
Heating Tape
Waste Incinerator
Reasons:
Present Currently
Fuel Temperature into Centrifuge
Cost

## Slide 16: WVO Storage
Image Source: www.automotivetools.com/Liquidynamics
Image Source: www.disasterstuff.com
Image Source: www.amazon.com
Vehicle Application
Notes: Options:
IBC Totes
55 Gallon Drums
5 Gallon Buckets
Conical Tanks
http://www.automotivetools.com/Liquidynamics/Tote-System-275-Gallon-IBC-Tote-Tank/901071/568/Product.aspx
http://www.disasterstuff.com/store/pc/5-PACK-of-Buckets-with-Standard-Lids-p66.htm#.Uo2nucSshcY
http://www.amazon.com/Gallon-Drain-Bottom-Inductor-Proces/dp/B003T42L7Y
Reasons:
IBC Totes:
  Shape
  Large Volume
  Openings & Valves
  Fork-Lift Access
  Food-Grade
5 Gallon Buckets
  Transportation
  Fryer Volume
Conical Tank
  Staging
  Bulk Sludge Removal

## Slide 17: Process Design
Rigid, Parallel System
*120 Sq. Ft
Wait 1 Month…
Vehicle Application
Notes: Options:
Non Rigid
Batch
Pull System
Hybrid
Reasons:
Cleanliness! (Rigid)
Settling Requirements
Raw VWO Output
Extra Capacity

## Slide 18: Raw WVO Transportation
Recycling Truck
Vehicle Application
Notes: Options:
Golf Cart
Recycling Truck
Reasons:
Stops Daily at Dining Halls
WVO is Form of Recycling
Zero cost or Added Labor

## Slide 19: Compost
Vehicle Application
Notes: Options:
Reuse
Compost
Dispose
Burn
Reasons:
Transportation Hassel
Environmentally Friendly
Fumes

## Slide 20: Costs
Upfront Component Costs:
  Pipes Pipe Connectors: $ 1,200
  Calvin Physical Plant labor: $ 600
  Valves & Actuators: $ 428
  Electronic Components: $ 185
  Total: $2,413
Monthly Operating Costs:
  Student Labor (Year 1): $ 450
  Student Labor (Year 2): $ 150
Vehicle Application
Notes: Get rid of totes on pricing

## Slide 21: A Biofuel Vehicle
Presented by: Mike Houtman
Notes: WVO can be used as a fuel….if you did not know

## Slide 22: How to Convert?
What Vehicle?
Vehicle Application
Notes: --->WE NEED TO CONVERT A VEHICLE, IT WILL NOT RUN ON IT’S OWN
2 main questions

## Slide 23: WVO Conversion
WVO criteria to be met:
  WVO Purge
  5 Microns
  160°F
  Diesel Engine
Image source: Greasecar.com
Image source: Dieseltronics
Image source: Glow Shift Direct
Image source: WVO Designs
Vehicle Application
Notes: When deciding what vehicle, certain criteria must be met:
Diesel for compression ratios
Purge to prevent geling
Microns to save injectors
Temperature to maintain flow viscosity

## Slide 24: Vehicle Yearly Usage (hours)
Chart: 
| Lawn Mower | Leaf Blower | Front Loader | Lift | Tractor | Dump Truck | John Deere
Yearly Run Time per Type [hr] | 2670 | 200 | 1072 | 100 | 200 | 50 | 20
Notes: There are many vehicles
3 mower models
Refer to the footer

## Slide 25: 2006 Toro GROUNDSMASTER 4000-D
Notes:   CRITERIA:
  Kubota diesel engine
  Leads operation time
  Expired warranty
  High visibility
  Duplicate conversion
  Nonessential vehicle

## Slide 26: Previous Experience
Notes: Previous colleges to implement or Consider a WVO vehicle include:
Bowling Green State University
Western Michigan
Bowdoin University
Furman College
Warren Wilson College

## Slide 27: Vendors
Notes: Warranty and Tech Support
2 ESTABLISHED Companies
Greasecar was selected, having an excellent customer service and tech support available

## Slide 28: Kits Available
Image source: Greasecar.com
Notes: contacted Greasecar, a non-specific conversion kit was quoted for this project.
Consisting of:
Additional coolant-heated tank
Additional filter, pump, valves, and hosing

## Slide 29
Image source: Greasecar.com
Notes: Diesel Tank
Heated WVO Tank
Heated Filter
Supply Valve
WVO Lift Pump
Injectors
Return Valve

## Slide 30: WVO Tank Location
WVO Tank
Notes: Tank size description
  21in x 8in x 12in (L x W x H)
  8.7 gallons
  5.5 hours of mowing
Placed above right fender
Trash Can may be moved

## Slide 31: Controller
Image source: Greasecar.com
Notes: electronic “Co-pilot” controller
automatically switches the supply valve to WVO based on a tank temperature sensor
Tells when to purge
  Cost: $300

## Slide 32: Controller Location
WVO Tank
Notes:   Where to put Co-Pilot?
  2 options:
    Directly onto operator control dashboard
    Tank upper surface

## Slide 33: Costs
The purchased equipment costs of this system derive from:
  Greasecar WVO kit: $1595
  Greasecar “Co-Pilot” controller: $ 300
  Calvin Physical Plant labor: $ 360
  Insulating tank cover: $ 40
  Total: $2295

## Slide 34: Long-Term Planning
Presented by Brandon Koster

## Slide 35: CERF Involvement?
Mower Maintenance?
Educational Outcomes?
Possible Expansion?
Notes:   How will Calvin prevent unforeseen issues and breakdowns that will come with a new fuel?
  How could Calvin expand this project in the future?
  How could this project be best integrated with the Calvin Energy Recovery Fund (CERF)?
  How could Calvin use this project to achieve desired educational outcomes?

## Slide 36
Fuel Injector Maintenance
Image Source ecx.images-amazon.com
Image Source: www.standardbrand.com
Notes: Get ride of totes on pricing

## Slide 37: Fuel Filter Maintenance
Image Source: www.vw-resource.com
Notes: Get ride of totes on pricing

## Slide 38: Engine Oil Analysis
Image Source: www.rockingsconsulting.com
Notes: Get ride of totes on pricing

## Slide 39: Testing Period
Image Source : bestclipartblog.com
Notes: Get ride of totes on pricing

## Slide 40: Additional Vehicle Options
Image Source: vimeo.com
Campus Safety Vehicle
Transportation Van
Notes: Campus Safety Vehicle
  Highly visible
  Must be reliable
    Lots of annual driving on poor roads
  Vehicle must be professional looking
Transportation Van
  Transporting Calvin groups (under 15 people)
  Options
    1999-2003 Ford E-350
    2002-2006 Dodge Sprinter
    1997-2001 Chevy Express Van

## Slide 41: New Vehicle Selection
2002-2006 Dodge Sprinter Van
http://www.moibibiki.com/images/dodge-sprinter-4.jpg
http://mbgtown.files.wordpress.com/2010/10/2008-sprinter-passenger-van-0061.jpg
Notes: 2002-2006 Dodge Sprinter Van
  Twice the MPG of Ford E350
  WVO conversion kits more widely available
  Better selection of acceptable used vehicles

## Slide 42: New Feedstock Sources
http://farm4.static.flickr.com/3201/2409592844_f382ca64a7_o.jpg
http://1.bp.blogspot.com/
Notes: Creative Dining Services
  Contacted Richard Balfour, Director of Dining Services at Calvin
    The colleges nearby have their own ways of disposal
Local Restaurants
  Contacted several restaurants located near Calvin
    A few small sized restaurants were willing to give their WVO
      Tokyo Grill, Mikado
    Hard for larger sized (Franchises) places to give their WVO
    Approximately 2-5 gal. per day per restaurant

## Slide 43: CERF Integration: Capital Funding
Notes: Overseeing fuel production
  CERF intern
    15 hours a month at $10 an hour total cost to college
Overseeing Mower Maintenance
  Physical Plant mechanics
    1 hour a month at $60 an hour total cost to college
    Additional preventative maintenance procedures relating to WVO fuel system supplied by ENGR 333 students
  Blue Project
    Energy saving projects that result in economic benefit for Calvin
    CERF provides project funding
    CERF pays itself from the energy/financial savings from break even plus 5 years
    Initial payback must be < 4 yrs
    Must be able to monitor the savings
  Green Project
    Energy or environmental project that does not have measurable cost savings or very long payback periods
    Demonstrate an environmental benefit for Calvin
    CERF has not yet funded a green project
Biofuel Blue Project Requirements
  Robust cost analysis must show < 4 yr payback
  Establish key measurables and how to record them
    Volume of raw oil retrieved from dinning hall
    Volume of usable oil
    Amount of normal diesel displaced by WVO
    Annual cost savings
Biofuel Green Project Requirements
  Payback > 4 yrs
  Show substantial environmental benefit: reduction of
    CO2, NOX, methane, particulate

## Slide 44: CERF Integration: Internship Program
http://www.chamaschools.org/wp-content/uploads/CLIPART_OF_32162_SMJPG_2.jpg
Notes: Overseeing fuel production
  CERF intern
    15 hours a month at $10 an hour total cost to college
Overseeing Mower Maintenance
  Physical Plant mechanics
    1 hour a month at $60 an hour total cost to college
    Additional preventative maintenance procedures relating to WVO fuel system supplied by ENGR 333 students
  Blue Project
    Energy saving projects that result in economic benefit for Calvin
    CERF provides project funding
    CERF pays itself from the energy/financial savings from break even plus 5 years
    Initial payback must be < 4 yrs
    Must be able to monitor the savings
  Green Project
    Energy or environmental project that does not have measurable cost savings or very long payback periods
    Demonstrate an environmental benefit for Calvin
    CERF has not yet funded a green project
Biofuel Blue Project Requirements
  Robust cost analysis must show < 4 yr payback
  Establish key measurables and how to record them
    Volume of raw oil retrieved from dinning hall
    Volume of usable oil
    Amount of normal diesel displaced by WVO
    Annual cost savings
Biofuel Green Project Requirements
  Payback > 4 yrs
  Show substantial environmental benefit: reduction of
    CO2, NOX, methane, particulate

## Slide 45: Educational Integration
Engineering 101
Fridays at Calvin
Annual Seminars
Prelude
Notes: Engineering 101
  Class tour of the vegetable oil facilities
  Hands-on experience
Friday’s at Calvin
  Advertise project to perspective students
    Through vocal methods and with a poster in the engineering building
  Explain lawn-mowers on campus tours
Engineering Seminars
  Annual seminar outlining project success and future

## Slide 46: Possible Senior Design Project: Automating the Production System
Two Electrical Concentrations
One Mechanical Concentration
One Chemical Concentration

## Slide 47: Costs
The monthly ongoing maintenance costs:
  1 hour Physical Plant Mechanic Time: $ 45
  Fuel Injector Additive: $ 16
  Fuel Filter: $ 15
  CERF Intern $ 180
  Total: $221/month

## Slide 48: Upfront Capital Costs
  Fuel Processing Costs: $ 1,972
  Vehicle Conversion Costs: $ 2,295
  Infrastructure Costs: $ 2,413
  Total: $6,680

## Slide 49: Monthly Operating Costs
  Fuel Processing Costs: $ 14
  Vehicle Conversion Costs: $ 221
  Infrastructure Costs: $ 150
  Total: $ 385

## Slide 50: Total Cost Analysis
Breakeven (w/ Student Labor)
Chart: Diesel vs. WVO
1
2
3
4
5
Notes: No blue line!
No October 2017!

## Slide 51: Proposed Timeline
Summer 2014
Construction
Winter 2014/15
Mower Conversion
Spring 2015
Begin Operation
Fall 2014
Senior Design Automation & WVO Collection

## Slide 52: Feasibility
Practically Feasible?
Economically Feasibility?
Environmentally Feasibility?
YES
YES
YES
Notes: Restate Question: What would it take to operate a biofuel vehicle using only on-campus resources?

## Slide 53
We recommend that Calvin operate one mower on WVO beginning April 2015.
Notes: 1 sentence recommendation
Environmentally Feasible
    Reduced emissions
      43% Carbon monoxide
      56% Hydrocarbons
      55% Particles
    Sustainability image on campus
    Educational opportunities
Fuel savings
  1300 gallons of diesel
Cost savings
  $4,000 of purchased diesel

## Slide 54: Questions?
Thank you for your time…

## Slide 55: Appendix

## Slide 56: Operating Procedure
WVO temperature
  The system must be started on diesel and the “Co-Pilot” will assist the operator in the fuel switch over
  Process takes approximately 5 minutes
System flush
  System must be flushed with diesel before final shut-down
  Process takes less than 1 minute
Fuel Usage
  The tank must be routinely at capacity to prevent air in the lines
  The tank must not be stored with WVO throughout winter
  The tank must be cleaned and inspected to prevent polymerization
  The fuel must be treated with additives to prevent bacterial growth

## Slide 57: Total Cost Analysis
Breakeven (w/ CERF Grant)
Chart: CERF Grant vs. No CERF Grant

## Slide 58: Tank Insulation

## Slide 59: Yearly Savings
Fuel savings
  1300 gallons of diesel
Cost savings
  $4,000 of purchased diesel

## Slide 60: Hardware Locations
Image source: Greasecar.com
Notes: Mounting of fuel lines, pump, valves, and filters by Physical Plant mechanic
After speaking with Physical Plant, the mechanic, Jeremy, is excited to work on the conversion kit

## Slide 61: Temperature Concern
WVO Tank
Vehicle Application
Notes: The largest concern comes from the tank temperature and its proximity to the operator:
  External surface of the tank may reach temperatures up to 200°F
  Upper tank surface is directly next to user dashboard

## Slide 62: Yearly Lawnmower Usage (hours/model)
Chart: 
| Mower 1 (4700D) | Mowers 2&3 (4000D) | Mower 4 (3280D)
 | 360 | 1680 | 630
Notes: There are

## Slide 63: Temperature Solution
Image source: Zoro Tools
Notes: Therefore, an insulating cover and warning label has been selected to protect the user from burn hazard.
Flexible Therma-Cel Polyolefin Pipe Insulation
2 sheets needed $18.95 each
Necessary for top and outer surface safety
http://www.zorotools.com/g/00058735/k-G3442731?utm_source=google_shopping&utm_medium=cpc&utm_campaign=Google_Shopping_Feed&kw=%7bkeyword%7d&gclid=CIiFgezslrsCFdE-Mgod4T4Acg

## Slide 64: Controller Location
Notes: In order to implement the “Co-Pilot” controller, it must be both visible and easy to access
2 main components

## Slide 65: Presentation Outline
Fuel Source
Vehicle Application
Transportation
Processing Plant
Waste
Biofuel Vehicle
Before:
After:

## Slide 66: Process Design
Rigid, Parallel System
Notes: Options:
Non Rigid
Batch
Pull System
Hybrid
Reasons:
Cleanliness! (Rigid)
Settling Requirements
Raw VWO Output
Extra Capacity

## Slide 67: Tank Dispense
Two Outlet, Float Dispense
Image Source: www.vegoilcar.co.uk
Notes: http://www.vegoilcar.co.uk/wvo_filtering_setup.php
Options:
1 Outlet
2 Outlet
2 Outlet (Float)
Reasons:
Fuel Quality

## Slide 68
Total Upfront Costs = $6,850

## Slide 69
Operating Costs = $236/month

## Slide 70: Valve Design
Actuator Controlled Valves
Image Source: www.praher-valves.com
Notes: http://www.praher-valves.com/files/big_images/Produkte/pvc/2W-KH-S4-pneum.jpg
Options:
Manual
Actuator Driven
Reasons:
Ease of Use
Safety
Ergonomics

## Slide 71: Valve Design
Actuator Controlled Valves
Notes: Options:
Manual
Actuator Driven
Reasons:
Ease of Use
Safety
Ergonomics

## Slide 72: Transportation Van Cost Analysis
Chart: Transportation Van Payback
| 41653 | 41684 | 41712 | 41743 | 41773 | 41804 | 41834 | 41865 | 41896 | 41926 | 41957 | 41987 | 42018 | 42049 | 42077 | 42108 | 42138 | 42169 | 42199 | 42230 | 42261 | 42291 | 42322 | 42352 | 42383 | 42414 | 42443 | 42474 | 42504 | 42535 | 42565 | 42596 | 42627 | 42657 | 42688 | 42718
Diesel Cost | 399.84 | 639.84 | 879.84 | 1119.84 | 1359.84 | 1599.84 | 1839.84 | 2079.84 | 2319.84 | 2559.84 | 2799.84 | 3039.84 | 3279.84 | 3519.84 | 3759.84 | 3999.84 | 4239.84 | 4479.84 | 4719.84 | 4959.84 | 5199.84 | 5439.84 | 5679.84 | 5919.84 | 6159.84 | 6399.84 | 6639.84 | 6879.84 | 7119.84 | 7359.84 | 7599.84 | 7839.84 | 8079.84 | 8319.84 | 8559.84 | 8799.84
WVO Cost | 2150 | 2300 | 2450 | 2600 | 2750 | 2900 | 3050 | 3200 | 3350 | 3500 | 3650 | 3800 | 3950 | 4100 | 4250 | 4400 | 4550 | 4700 | 4850 | 5000 | 5150 | 5300 | 5450 | 5600 | 5750 | 5900 | 6050 | 6200 | 6350 | 6500 | 6650 | 6800 | 6950 | 7100 | 7250 | 7400
Result: 1.5 year payback time
Notes: Assumptions
  Fuel system capital costs already sunk for lawn mower
  24,000 miles a year, 2,000 miles a month
  Only $150 more operating cost per month to